|  | Injury & Illness Prevention Program Job Safety Analysis Form |
| --- | --- |
|  | 501 Westwood Plaza, 4th Floor • Los Angeles, CA 90095 Phone: 310-825-5689 • Fax: 310-825-7076 • www.ehs.ucla.edu |

| Picture of task/equipment: | Task: | Cordless power drills |
| --- | --- | --- |
|  | Name of Shop or Dept: | OCH Maintenance, UA, LACC |
|  | Job Title(s): | Building Maintenance staff |
|  | Analyzed by: | M. Williams |
|  | Date: | 04/29/13 |
| Required PPE: |
| Work boots Gloves hearing protection safety glasses |
| Required/Recommended Trainings: |
| STF Safety Equipment safety precautions |
| TASK | HAZARDS | CONTROLS |
| Using a cordless power drill | Lacerations Punctures Slip Trip Fall Burns Struck by’s | Don PPE, including safety glasses, work boots and gloves. Additional PPE should be worn such as a dust mask or hearing protection when working around wood or metals dust and/or loud ambient noises respectively. Before use make sure drill bits are sharp and not cracked as they can break off creating injury. Do not wear loose fitting clothing that can get caught in moving parts. Keep hair and jewelry out of the drill path as well. Do not over push, modern drills have a lot of torque and a long battery life. Let the drill do the work. Use higher drill speeds for wood and lower drill speeds for metal. If working on small items, use a clamp to secure the item you are drilling. Use both hands to securely hold the drill whenever possible, this will prevent it from slipping and/or spinning out of control. Continuous use of the drill can cause vibration. Make sure to take short breaks at frequent intervals to rest hands. When drilling is complete, be careful not to touch the drill bit, it is often extremely hot initially. Give it time to cool off. |